## Slide 1: KIE1008 PROGRAMMING II ASSIGNMENT
Team members:
Man Kai Sheng 22004646/1
Yap Jing Wey 22004647/1
Yvone Loh Jing Yi 22004615/1
Lee Yin Shao 22004677/1

## Slide 2
Schematic drawing

## Slide 5
Composition
OOP Element
Object of one class as a member data of another class
Motor
Motion
In Motion class,
we create objects
(leftMotor, rightMotor) of
Motor class

## Slide 6
Inheritance
Consists of base class and derived class, new class inherits the members of existing class
LeftSensor.h
RightSensor.h
Base class: UltrasonicSensor
Derived class: FrontSensor
We also implement inheritance in LeftSensor, RightSensor class:
Constructor in FrontSensor class:

## Slide 7: Hardware Limitations 1 2 3
Power Supply
Batteries (low power) runs out quickly
Insufficient memory
Have to use Arduino Mega 2560 Pro with larger memory than Arduino Uno
Precision in Position Control
We use IMU sensor instead of encoder
Arduino Uno - Program memory (32 kilobytes) and RAM (2 kilobytes)
Arduino Mega 2560 Pro - Program memory (256 kilobytes) and RAM (8 kilobytes)
Energizer (Non-Rechargeable Battery) – Expensive, Hold longer
Beston (Rechargeable Battery) – Run out quickly, takes long time (approximately 2 hours) to charge
9V battery is insufficient to support both motor driver and arduino
Encoders: Provide real-time feedback, enabling the robot's control system to make immediate adjustments to ensure straight-line motion. Move from one cell to another cell with the precise distance
IMU: Require additional processing to derive position information, which might introduce delays. Integration error: accumulation of errors that arise during the process of integrating angular rate measurements over time

## Slide 8: Software Limitations 1 2 3
Limited Development Environment Features
Arduino IDE is designed for simplicity, lacking some features found in more advanced development environments.
Algorithm Complexity
We keep the maze-solving algorithm simple and well-optimized to ensure that it can run effectively on the Arduino Mega 2560 Pro without exceeding its computational capabilities.
Absence of encoder coding
Without encoder data, the reliance on other sensors, such as ultrasonic sensors, becomes more critical for navigation.
We import TimedAction library which initially do not have in Arduino IDE
- Inaccurate distance - Hard to control speed - Susceptible to uneven surfaces, variations in wheel slippage, or changes in battery voltage

## Slide 9: Robot Budget Table

## Slide 10
Thanks!